Will McNeill
18 April 2012
HPC Lab 8
NUMA, KMP, OpenMP/MPI Hybrid

1. Running stream_numa with numactl –interleave=all results in significantly faster benchmarks. We can attribute this to numa's memory policy placing chunks of memory in better places, allowing it to be accessed faster. This memory policy reduces the need to use memory on a different socket, thus reducing the need to use the interconnect, and reducing the associated time penalty.

2.
A-Setting KMP_AFFINITY to scatter results in faster benchmarks.
B-This is because scatter places threads as far apart from each other as possible. This distributes the threads across both sockets, allowing for maximized memory bandwidth, as we are using memory on both sockets. Compact places threads as close to each other as possible. This means all threads are on the same socket and share the same memory, which incurs a memory bandwidth penalty. Individual threads do not have to synchronize frequently in this example, making scatter the better policy. If threads had to communicate a lot or operate on lots of the same memory, scatter would not have such a strong advantage.

3.